## Slide 1: FEEL BEFORE YOU BUILD
Hands-on prototyping with actuators · 2 hours
Notes: 0:00. Start here, and do not read the slide.
Open with the demo, not with talking. Have the coin motor and the solenoid both
wired and running before anyone sits down.
Buzz a phone-style notification on the motor. Then send the same message on the
solenoid. Ask which felt more urgent. Let them answer. Nobody needs theory for
that, and it is the argument for the whole session.

## Slide 2: TLDR
Two hours finding out what actuators feel like, and leaving able to drive one from your own code.
Get a board and run task 01. Something spins.
Change two numbers, upload again. That loop is the workshop.
Pick up the actuators you are not driving.
Work through as many of the five tasks as you get to.
Build one signal someone else can read without looking.
Notes: Fifteen seconds. It is a map, not a talk.
Useful because half the room arrives expecting a lecture and needs to be told
immediately that this is not one.

## Slide 3: WHY WE ARE HERE
You can read a datasheet. You have never held one of these.
Most projects end up on the screen and the speaker
• Not because touch was wrong
• Because nobody knew the lab has 117 coin motors
Today: decide it feels cheap, pick something else
• Better now than in week 46
Notes: Say the full version out loud, the slide only carries the skeleton:
"You can read a datasheet. You have never held one of these. Today you put a
vibration motor against your own wrist, decide it feels cheap, and pick
something else. Better now than in week 46 with the demo three days out."
Every year projects end up on the screen and the speaker, and touch gets
designed on paper then dropped. Two minutes, then move.

## Slide 4: HOW TODAY WORKS
A board each. You build the circuits yourself
• Every part, every wire, from an empty breadboard
Two or three stations each, getting harder
• Start with two wires. End with a transistor
Actuators are on the tables at the front
• Go and feel the ones you did not build
Finish by building one signal someone else can read
Notes: Set the shape clearly, because it is not a lecture and they will wait to be
lectured at.
A board each, and they build the circuits themselves from an empty breadboard.
Say that plainly, because a room of computer scientists will assume the
hardware is someone else's problem and wait to be handed a working rig.
Two or three stations each, in rising difficulty. Nobody builds all six.
The ladder does the teaching: task 00 is two wires, task 04 is one, task 05
joins them, and only then does task 01 introduce a transistor. By the time
they meet a driver circuit they have already had three things work, which is
what makes them willing to debug the fourth.
The actuators they are NOT building sit on tables at the front. Tell them
explicitly to go and pick those up between builds.

## Slide 5: RUN SHEET
Times are offsets from the start. The only hard checkpoint is 0:25: everyone has task 01 running.
0:00 10 min Two motors, same message. Which felt urgent?
0:10 10 min Breadboards out. Piezo: two wires, everyone
0:20 20 min Task 01: your first driver circuit, together
0:40 45 min Build on, at your own pace
1:25 10 min Round-the-room: what surprised you
1:35 20 min Blind test on task 05
1:55 5 min Pack down
Notes: Show it, do not narrate it. Fifteen seconds.
Two hard checkpoints. At 0:20 every single person should have a piezo ticking,
because that is two wires and if it is not working the problem is the board or
the IDE, not the circuit. Fix those before anyone meets a transistor.
At 0:40 most people should have task 01 buzzing. If someone is still fighting
it, pair them with a working group rather than leaving them to debug alone.
Walk the room during the 45 minute block. Look for reversed diodes and
transistors in backwards; both fail silently and neither is guessable.

## Slide 6: THE TASKS, IN BUILD ORDER
Each one adds a single new thing to the circuit before it.
00 Make it tick piezo 2 wires
04 Make it notice you wire and foil 1 wire
05 Make it answer both of the above 3 wires
07 Make it turn stepper 6 wires, a trap
01 Make something spin coin motor + transistor
02 Make something tap solenoid + own supply
03 Make something warm Peltier tile + H-bridge
Two or three each. Nobody does all of them.
Notes: Ninety seconds on this slide, no more.
Read it as a ladder, because that is what it is. The top three need no
transistor at all: piezo, foil pad, then the two joined together. That is a
complete sense-and-respond loop built from three wires, and they can have it
working inside twenty minutes.
The bottom three each add exactly one new idea. Task 01 adds a transistor and
a flyback diode, because a motor draws 100 mA and a pin gives 40. Task 02 adds
a separate supply. Task 03 adds an H-bridge for direction.
Say clearly that nobody is expected to do all six, and that two done properly
beats five rushed.
Task 05's last experiment IS the closing brief, so the work carries over.

## Slide 7: HOW THE TASK SKETCHES WORK
Wire it from the diagram at the top, then upload. All of them: github.com/labtools-au/multimodal-actuator-workshop
A PINS block at the very top
• Every leg, every wire. Build from that, not from memory
A CHANGE ME block below it
• Two or three numbers. Edit, upload, feel the difference
A THINGS TO TRY list at the bottom
• Four experiments. The last is the interesting one
Notes: Say the format once here rather than repeating it per task.
PINS at the very top: every leg and every wire. That block is what they build
from, and it is why nobody needs a schematic. Point at it explicitly.
CHANGE ME below that: two or three numbers, already set to something that
works. THINGS TO TRY at the bottom: four experiments, easy to hard, and the
last one usually asks for a rewrite rather than a tweak.
Upload problems, in the order they will hit you:
* wrong board or port under Tools
* ADCTouch not installed (tasks 04 and 05)
* solenoid task: board resets when it fires means its supply is off
Write the repo URL on the whiteboard now. It gets asked for six times.
If a task's hardware fails, utils/ has the diagnostics: pin_sweep, i2c_scanner,
analog_monitor.

## Slide 8: PIN MAP
01 spin D9 PWM 1k to PN2222 base, motor on collector
02 tap D6 MOSFET gate, own supply, grounds joined
03 warm D3 + D5 PWM H-bridge low and high, bench supply
04 sense A0 bare wire to foil. That is all of it
05 answer A0 + D9 the pad, plus any actuator
07 stepper D8 D9 D10 D11 ULN2003 IN1 to IN4
Only D3, D5, D6, D9, D10, D11 do PWM. Stepper pins go into the constructor OUT of order: 8, 10, 9, 11.
Notes: Reference, not a talking point. Ten seconds, or skip it entirely if the
stations are already built.
It earns its place two ways: you use it while setting the room up, and it is
the slide to jump back to when someone asks "which pin was the solenoid".
The bottom line is the one worth reading aloud if anyone touches the stepper:
the pins go into the constructor OUT of order, 8, 10, 9, 11. Wired in numeric
order it buzzes instead of turning and looks like a dead motor.

## Slide 9: WHAT YOU GET IN THE BASE KIT
One set per pair, collected before you start task 01. Below: the three parts people always come back for.
Board, breadboard, jumper wires, resistors: on the tables.
Not in the drawers, so take what you need.
Breadboard supply, 8A. Anything past an LED.
L9110S H-bridge, 2C. Reversing, and the Peltier.
PAM8403 amp, 11F. A transducer needs one.
Notes: Hand this out before anything else, or you will spend the session
fetching parts one at a time.
One set per pair. The three drawer numbers are the ones people actually come
back and ask for: 8A breadboard supply, 2C H-bridge, 11F amplifier.
Jumper wires, breadboards and resistors are not tracked in the component
database, so make sure there are enough on the tables before students
arrive.

## Slide 10: VIBRATING MINI MOTOR DISC
An off-centre weight on a motor shaft, sealed in a disc. The same part as in your phone.
Feels like: a buzz you cannot make gentle and fast at once.
USED FOR
Phone notifications, controller rumble, anything worn under clothing.
1E | 117 | 2.5-3.8V rated | 100 mA at 5V | PWM
Notes: The one everybody already owns without knowing it. Every phone has one.
The point worth making: speed and strength are welded together. That single
constraint is why the other five exist.

## Slide 11: PIEZO ELEMENT
A crystal that flexes when you put current across it. Near-instant, almost no power, but shallow.
Feels like: a tick, not a thump.
USED FOR
Clicks and confirmations. Anything where lag would feel broken.
Drawer 6F | 69 in stock | any digital pin
Notes: The escape from the coin motor's compromise. A crystal that flexes when
you put current across it: near-instant, almost no power, but shallow.
A tick, not a thump. Point anyone here who needs something to feel responsive
rather than just present. 69 in the drawer, so nobody has to share.

## Slide 12: MINI PUSH-PULL SOLENOID
A coil that yanks a metal rod when you energise it. No half a tap: it fires or it does not.
Feels like: a person tapping you, not a machine signalling.
USED FOR
Navigation cues on the body, braille cells, alerts in noise.
3E | 24 | 5V, 1.1 A, 4.5 ohm | 3mm throw, 80g
Notes: Pass this one around if you can. It is the one people remember, because a
knock reads as a person rather than a machine.
Warn them now that it needs its own supply, so it does not come as a surprise
at task 02.

## Slide 13: CAPACITIVE PAD
A wire taped behind foil, card or fabric. No sensor and no breakout board, which is why the box on the left is empty.
Feels like: nothing. That is the point. The surface stays plain.
USED FOR
Invisible controls in wood or fabric, waterproof panels.
No drawer, no part number, no cost. Any analogue pin
PHOTO
Capacitive pad
Notes: Hold up a wire and a piece of foil. That is genuinely the whole sensor.
This is the slide that changes what people think is possible, because it costs
nothing and hides completely inside a prototype.

## Slide 14: PELTIER TILE
Heats one face and cools the other. Flip the current and it reverses.
Feels like: slow. Several seconds before you are sure which way.
USED FOR
Slow ambient state. Never an alert.
Drawer 4C | 25 small, 35 big | needs an H bridge
Notes: Say the honest limitation out loud: it is slow, and hot alternating with
cold just reads as lukewarm.
Good for slow ambient state. Wrong for alerts. Saying so here saves a project
from finding out in week 46.

## Slide 15: SURFACE TRANSDUCER
Turns any surface into a speaker. Drive it so one frequency is felt and another is heard, from the same part.
Feels like: more certain, rather than louder.
USED FOR
Noisy or bright environments, and accessibility.
Drawer 7F | 12 large, 13 medium, 23 bone | needs an amp
Notes: The redundancy argument. Same driver, one frequency you feel and one you
hear.
Together is not louder, it is more certain. Cheapest reliability a project can
buy, and it is also the accessibility answer.

## Slide 16: SERVO
A motor that holds a position instead of spinning freely. Tell it an angle and it goes there.
Feels like: something deliberate moving, with force behind it.
USED FOR
Anything that points, pushes, opens or resists a hand.
Drawer 2F | 80 in stock | Servo.h | needs its own 5V
Notes: Worth showing even though it is not in a task. Most projects that need
something to physically move end up here rather than on a vibration motor.
80 in stock, so nobody has to share.

## Slide 17: STEPPER MOTOR
Moves in fixed steps rather than continuously, so you always know where it is without a sensor.
Feels like: precise, and audibly clicky.
USED FOR
Slow accurate motion. Dials, sliders, anything positioned.
2A | 44 | ULN2003 driver | 2048 steps/rev
Notes: The precision option. Moves in known steps, so you can position it
without any feedback sensor at all. 2048 steps per revolution.
Needs a ULN2003 driver board, drawer 2A, 27 of them.
If anyone tries one: the Stepper constructor does NOT take the pins in numeric
order. Wire IN1 to IN4 on pins 8 to 11, then write Stepper(2048, 8, 10, 9, 11).
Get it wrong and it buzzes and jitters instead of turning, which looks like a
dead motor. bench_tests/07_stepper has it right, with the note.

## Slide 18: ELECTROMAGNET
Grabs and releases ferrous metal on command. No moving parts of its own.
Feels like: a grip that appears and vanishes.
USED FOR
Latches, holds, and anything that should let go on cue.
Drawer 3D | 17 mini, 11 standard | needs a MOSFET
Notes: The one people forget exists. It grabs and lets go, with nothing moving.
Good answer for anything that should hold and then release: a latch, a door, a
thing that falls when the event happens.

## Slide 19: FREESTYLE, WITHIN THREE LIMITS
You do not have to do the tasks in order, or finish them. Playing properly with two beats rushing all five.
If you want to drive something not in front of you, go get it.
The three things that are not negotiable
• Solenoid and Peltier get their own supply, never USB
• The Peltier heatsink goes on before it is switched on
• No motor straight from a pin. 40 mA limit, it wants 75
Notes: Two messages on one slide, and they pull in opposite directions on
purpose. Say the permission warmly, then change tone for the limits.
Permission first: some students will not believe they are allowed to skip
ahead or stop early unless told. The failure mode is a pair rushing all five
badly instead of doing two properly.
Then the three hard limits, and here you should sound firm. Say the numbers
out loud: a pin gives 40 mA, the motor wants about 75. It is not a rule they
have to take on faith.
Worth adding: a board resetting when the solenoid fires is a POWER problem,
not a code bug. That saves someone twenty minutes.

## Slide 20: THE ONE THAT SURPRISES PEOPLE
Touch input for the price of a wire. The thinking is where it costs you.
Threshold is relative, never absolute
• Readings drift with humidity and mains hum
• Fixed threshold works at 9am, fails at 1pm
Baseline only learns while untouched
• Or a long press teaches it that a finger is normal
Notes: Slow down here. This is the single idea most worth stealing from today, and
it is worth interrupting the room for once most people have reached task 04.
Two things students get wrong:
1. A fixed threshold. Works in the morning, fails after lunch, because the
reading drifts with humidity and mains hum.
2. Feeding the baseline buffer always. A long press then teaches the baseline
that a finger is normal, and the touch silently stops working. The buffer
must only learn while untouched.
Put the Serial Plotter on the projector. Watching the baseline wander while the
trigger line tracks it explains the whole design in ten seconds.
For what it is worth, the rig this came from went through the same tuning: an
earlier version used 1.008 with a 50-sample baseline, the final one 1.01 with
25. Everyone tunes these.

## Slide 21: INPUTS, AND PRIOR ART
Notes: 1:25. Pull the room back together.
One sentence per group: what surprised you. No slides, no laptops. Ten minutes.
Expect someone to report the Peltier delay. Let that land, it is far more
persuasive from a peer than from you.

## Slide 22: INPUTS WORTH KNOWING ABOUT
One table with a sign. Wander over between tasks.
• Capacitive touch. A wire. That is task 04
• GSR, drawer 0C5. Exactly one in the lab, so ask first
• Your own phone. No soldering at all
Force (FSR), 4A. 46 tiny, 33 square. Calibrate each one.
Flex, 4B. Only 8 left, so share them.
Pulse, 9D. 9 in stock. Steady at rest, useless once moving.
Notes: Mention, do not teach. These sit on one table with a sign.
The honest warnings matter more than the specs: PPG is useless once the hand
moves, GSR drifts so only relative change works, FSRs need per-pad calibration.
Push the phone option hard. For a lot of projects it beats everything else on
the table and needs no soldering at all.

## Slide 23: YOU ALREADY WRITE CODE. WHY COME?
Fair question. Three honest answers.
You cannot Google what something feels like
• No datasheet says a knock reads as a person, a buzz as a machine
The parts are free and already here
• Borrowing beats ordering. Nothing to buy, nothing to wait for
Your devices hide sensors you may not be able to reach
• Find out today which open up, and which are locked
Notes: The slide that earns the room's attention, so do not rush it.
This audience can write the code already, and they know it. Saying so out loud
buys credibility for the rest. The argument is not "you need to learn to
program a motor", it is "you cannot Google what something feels like".
The second point is practical and lands with everyone: the parts are free and
already in the building.

## Slide 24: REVERSE ENGINEER WHAT YOU ALREADY OWN
The trackers in your pocket and on your wrist. What opens up, and what does not.
BLE heart rate strap: readable from a web page
• Web Bluetooth, standard GATT. Chrome and Edge only
Most Garmin watches: the same, with no app
• Turn on Broadcast Heart Rate and it acts as a strap
Apple Watch: nothing live, whatever you write
• HealthKit needs a watchOS app in Swift
Garmin history: Connect IQ, or the API afterwards
• Good for analysis. Useless for reacting in real time
Notes: The slide the tinkerers will care most about, and the one where being
precise matters, because the internet is full of wrong answers.
The useful surprise: most Garmin watches broadcast heart rate over BLE
natively. Turn on Broadcast Heart Rate, or start a Virtual Run, and the watch
appears as an ordinary heart rate strap that Web Bluetooth can read from a web
page. No Connect IQ app, no SDK, no API key.
Apple Watch will not. HealthKit needs a companion watchOS app in Swift, so
third-party apps that re-broadcast over BLE are the practical route.
Web Bluetooth is Chrome and Edge only. Not Safari, not Firefox. Same lesson as
vibration: check the feature before it goes in a plan.
Good project prompt if anyone wants one: a page that pairs with a strap and
drives an actuator from a live pulse. That is an afternoon.

## Slide 25: WHAT A PHONE WILL AND WILL NOT GIVE YOU
Open sensors.chomskylab.dk on your own phone right now.
Works in a web page
• Accelerometer and gyroscope, microphone, camera
• Pointer pressure, though a trackpad reports only 0 or 0.5
Does not, whatever the tutorial says
• Phone vibration on iOS. WebKit has never shipped it, at any version, and Chrome on iOS is Safari underneath
So "the phone buzzes" works on no iPhone in this room.
• Check the feature, not the tutorial, before it is in a plan.
sensors.chomskylab.dk
Notes: Have them open sensors.chomskylab.dk on their own phones while you talk.
The split between what works and what does not lands far harder on their own
device than on a slide.
The bottom half is the single most useful fact here, and the one people get
wrong because a blog post said otherwise.
Say it plainly: iPhones do not vibrate from a web page. Not with a polyfill,
not with a library, not in Chrome for iOS, which is Safari underneath.
The general lesson is bigger than vibration: check the feature on caniuse
before it goes in a project plan, not after. Two minutes now against a
rewrite in week 46.

## Slide 26: TWO RIGS THAT ALREADY EXIST
Built here, by students at roughly your stage.
Moving screen, Arduino Uno
• Breathes when idle. Retreats when touched
• Easing and idle motion do the work. A dozen lines
Instrumented sock, ESP32
• Six force sensors under a foot, batched over Wi-Fi
• Calibrate per sensor. Batch your writes
Notes: Five minutes, and put the actual repos on screen if you can.
The argument: this was built by students at your stage, not by a lab with a
budget. The gap between "we should use touch" and "it moves when you touch it"
is smaller than it looks.
The moving screen has a browser control panel over the serial port, which is
what you will wish you had at the project demonstrations.
Note for you: the sock repo has a hardcoded Wi-Fi password and live patient IDs
in it. Scrub before showing, or show only the calibration section.

## Slide 27: BUILD ONE SIGNAL
Notes: 1:35. The blind test.
Most groups will already have something from task 05. This is where it gets
tested by someone who did not build it.

## Slide 28: THE BRIEF
30 minutes. Not long enough to be precious about it.
One actuator, whichever you built
• Three messages: arrived, something wrong, finished
Vary rhythm above all
• Piezo: rhythm is all you have. Motor: strength too
Blind test: they name all three
• Note which two got confused, and why
Notes: Read the brief out once, then get out of the way. Full wording, since the
slide is only the bones:
"Pick one actuator. Encode three messages: arrived, something wrong, finished.
Vary only the rhythm of the pulses and how strong they are. Then hand it to
another group with the screen turned away and see if they can name all three."
If someone asks to add a second actuator, say no. The constraint is the
exercise.

## Slide 29: THE CONSTRAINT THAT MATTERS
The recipient cannot look at the device.
If it only works while someone watches a screen,
you built a visual interface with a motor glued to it.
Notes: The line worth repeating twice.
Run the test: swap groups, receiver looks away, guess all three.
Then have each group name which two got confused and what would have separated
them. That confusion is the actual learning, not the successful ones.

## Slide 30: BEFORE YOU CALL IT DONE
Hand your device to another group with the screen turned away.
• They can tell all three messages apart
• It does not fire continuously when held
• You know which two got confused, and why
What you actually leave with
• What things feel like, how to drive one, and which to pick
• That last one is the expensive mistake this prevents
Notes: Put this up while the blind tests run, so groups can check themselves
without asking you.
The middle line matters most: a device that fires continuously when held is
the single most common bug, and it is a debounce problem.
Then close on the bottom half, thirty seconds. If they leave with one thing,
make it the last point: pick the actuator before designing the interaction.
Discovering in week 46 that the chosen one cannot do the job is the expensive
mistake this session exists to prevent.

## Slide 31: GO AND TOUCH THINGS
Everything is open: code, slides and session plan
github.com/labtools-au/ multimodal-actuator-workshop
Notes: Point them at the repo. Every task sketch is commented for them, and the
bench test sketches are there too if they want to see the minimal version.
Last thing to say: pick your actuator before you design the interaction, not
after. Today was so they can do that from experience rather than a datasheet.
Pack down: everything back in the box, including the resistors. It will not all
come back.
If anyone wants to borrow parts for the project weeks, now is when they ask.